## Slide 1: Robotics Competition
Team 1: Andrew Samboy, August Gress, Ben Vonderheide, Rhea Gogia, Kevin Zheng

## Slide 2: Thought Process
How to make turns by adjusting the motor speed
How to recognize dead ends
How to not make the same mistakes on the second run
How to handle curved and diagonal paths
How to find the most optimal path

## Slide 3: Code Design
Algorithm is based on the left hand rule
When faced with an intersection, the robot will always turn left rather than turning right or going straight
The robot records the path it takes with (L, R, S, or B)
After the first traversal the robot eliminates dead ends by replacing certain patterns such as (LBL, with S)
The second traversal then takes the shortest path

## Slide 4: Challenges
Giving a smaller delay time after dead ends so that the robot wouldn’t overturn
Finding the optimal speed when making turns
  Adjusting motor speed to get a more accurate path
Balancing priorities between speed and accuracy